## Slide 1: Communication protocol RS485
Tiefighters

## Slide 2: Settings on the Pi side
912600 baudrate with 1 start bit, 8 data bits, 1 stop bit.
The Raspberry Pi will send its function along with the target sensor to the RS485 bus and calculate the duration of the signal it requests to the sensor.
Based on the calculated duration the Pi will set a timeout and start reading the bus.
We need some form of flow control to give the Pi time to read and flush the buffer. We should also test if the Pi can read the buffer fast enough to handle the incoming datarate
Open question: how do we check for parity?
Open question: how do we control the flow for the Pi to flush the buffer?

## Slide 3: Acoustic features
Time-domain
Time-of flight
Rise time
Settling time
Peak amplitude
Time domain energy
…
Frequency-domain
Peak power and peak frequency
Harmonic ratio
Partial power (between frequencies)
Spectral centroid
Spectral kurtosis
…

## Slide 4: Metadata
Sensor number
Pi number
Function type
Function parameters
Timestamp

## Slide 5
IoT Core IoT Rule
MQTT
S3 Int Storage Red.
Block Feature extraction
Sine Feature extraction
Lambda - Reduction
Time-of-flight
S3 Int Storage full
Kinesis firehose
Timestream DB
Eventbridge

## Slide 6
Eventbridge
IoT Core
Pi code loop
Greengrass
Continuous buffer reader
Raspbian Lite
Very high priority
Low priority
Medium priority
Key considerations
Real-time requirements || Buffer sizes and flow control || Testing and monitoring
Manager
High priority
Sine pulse
MQTT Function: Sine pulses, frequency, add/remove sensors
Block pulse
Time-of-flight

## Slide 7: OLD

## Slide 8: Pi code structure – Block
Manager
Continuous buffer reader
OS (Pi Lite)
Very high priority
Low priority
1 GB, 0.25 Clock
Medium priority
Key considerations
Real-time requirements || Buffer sizes and flow control || Testing and monitoring
FFT &
Reduction
High priority
1 GB, 0.25 Clock
Feature extraction
Preprocessor
High priority
Feature extraction
Time-of-flight
Very high priority

## Slide 9: Pi code structure – Sine
Manager
Continuous buffer reader
OS (Pi Lite)
Very high priority
Low priority
1 GB, 0.25 Clock
Medium priority
Key considerations
Real-time requirements || Buffer sizes and flow control || Testing and monitoring
FFT &
Reduction
High priority
1 GB, 0.25 Clock
Feature extraction
Preprocessor
High priority
Feature extraction
Time-of-flight
Very high priority

## Slide 10: Pi code structure – TOF
Manager
Continuous buffer reader
OS (Pi Lite)
Very high priority
Low priority
1 GB, 0.25 Clock
Medium priority
Key considerations
Real-time requirements || Buffer sizes and flow control || Testing and monitoring
FFT &
Reduction
High priority
1 GB, 0.25 Clock
Feature extraction
Preprocessor
High priority
Feature extraction
Time-of-flight
Very high priority

## Slide 11
Pi code structure
Manager
Continuous buffer reader
OS (Pi Lite)
Very high priority
Low priority
1 GB, 0.25 Clock
Medium priority
Key considerations
Real-time requirements || Buffer sizes and flow control || Testing and monitoring
FFT &
Reduction
High priority
1 GB, 0.25 Clock
Feature extraction
Preprocessor
High priority
Feature extraction
Time-of-flight
Very high priority

## Slide 12
Manager
Manager
Block pulse reduction
Sine pulse reduction
Time-of-flight
Block Feature extraction
Sine Feature extraction
Kinesis data firehose
IoT Core IoT Rule
MQTT
S3 Storage
Timestream DB

## Slide 13
Greengrass+ Lambda
Block pulse reduction
Sine pulse reduction
Kinesis data stream
IoT Core IoT Rule
MQTT
Time-of-flight
S3 Storage
Block Feature extraction
Sine Feature extraction
Timestream DB
AWS Lambda - Manager
Time-of-flight

## Slide 14: Learning step 1
Greengrass+ Lambda
Light sensor data
Kinesis data stream
IoT Core IoT Rule
MQTT
S3 Storage
Block Feature extraction
Sine Feature extraction
Timestream DB
AWS Lambda - Manager
Time-of-flight

## Slide 15
Greengrass+ Lambda
Light sensor data
IoT Core IoT Rule
MQTT
S3 Storage
Timestream DB
AWS Lambda
Block Feature extraction
Sine Feature extraction
Kinesis firehose
Trigger
Router
Fog