## Slide 1: Function design M9
03-11-2023

## Slide 2: Traditionele sine sweep

## Slide 3: Onze frequentie range
Wij willen in de breedste setting frequenties tussen de 5 kHz en 100 kHz meten. Onder de 5 kHz hoeft niet dus de langst durende frequentie duurt maar 0.2 ms en dit gaat hard omlaag.

## Slide 4
PWM instruction
Sine instruction
PWM Frequency
(F)
Amount of pulses (Y)
(N) Burst measuring cycles
Pulse 1
Pulse N
Wait between bursts (X)
Function: PWM_Burst(F,X,Y,N,A,B)
Sweep 1
Sweep N
Min. Frequency (Fmin)
Max. Frequency (Fmax)
Wait 5 ms between bursts
Function: Sine_Burst(Fmin, Fmax,R, N,A,B)
N Sweep measuring cycles
Pulse amplification factor (A)
Microphone amplification factor (B)
Pulse amplification factor (A)
Microphone amplification factor (B)
Sweep duration (15 ms)
Amount of repetitions (R), here shown as 1

## Slide 5: Parameter max-min values: Sine
Vast: 15 ms sweep, 5 ms wachten tussen sweeps
A: Voltage ranges from 0-10 V
B: To amplify Infineon mic (-73 dB noise level)
N: Maximum of 10
R: 1 to 5 repetitions
Fmin: 5 kHz
Fmax: 100 kHz

## Slide 6: Time-of-flight meting
M91200 X Plense

## Slide 7
TOF instruction
Sine instruction
PWM Frequency
(Fres)
(N) Burst measuring cycles
Pulse 1
Pulse N
Wait between bursts (X)
Function: TOF(Fres,X,N)
Pulse amplification factor fixed
Microphone amplification factor fixed

## Slide 8: Tone burst
(N) pulses
(A) amplification
factor
(F) Frequency
Amount of repetitions (R), wait time between repetitions: 10 ms

## Slide 9: Next step
Calculate the average over the repetitions