## Slide 1: Hardware
08-04-2024

## Slide 2: Embedded CPU: EdaTec CM4 Sensing
CM4 based compute
  We choose 4 GB RAM, 8 GB eMMc, Wifi/Bluetooth on
  Add a 128 GB SD Card for the data
  Contains an RTC based clock
  Contains a 4G/LTE module
  Contains the capability to read an SD card next to the eMMc
Missing:
  UPS (for power outage) module
Open questions long term:
  Do we need the 8 or 4 GB RAM version, do we need Wifi, do we need more cooling

## Slide 3: Storage use
eMMc
Contains the OS and essential services
Contains the Docker engine
Contains the core Docker Image
SD-card
Contains the home directory
Contains data and logging
Contains the containers
Does not contain a Rpi image

## Slide 4: Additions to the module
A plate with the Plense logo blocking off usb/Hdmi ports
An extra part over the RS-485 and 12V stick out containing the 12V cable splitter, two wartels (1 for the RS485 out and 1 for the 12V in)

## Slide 5: Wiring RS485, we need two UART channels
NOTE: we need AMA2 for RS485-1 and AMA3 for RS485-2,
For an extra one we would need AMA1 (3) and AMA4 (4)

## Slide 6: Current use per sensor
Not more than 30 mA
Max current we can apply over the wire: 1 A
The ear and main RS485 connectors are already switched so we do not have to twist the wires to connect receiver to transmitter and vice versa
The grounds on the EdaTec are all connected

## Slide 7: Important questions
Do we see clock frequency throttling
  Internal temperature
  Not enough current supplied
  Underclock if possible?

## Slide 8: Required materials
3D printer?
Foam
Waterproof 2/3A 12VDC chargers
If the EdaTec works well
12V cable splitter
Print protecting the RS ports
TODO 3D print design
How to make the SHT touch outside air and protect insides

## Slide 9: Supplementary information

## Slide 10: Handling the CM4: use plastic tool

## Slide 11: Possible settings to implement
We can turn off a lot of power and CPU consuming components
  Make sure the Pi doesn’t heat up too much
  Underclock
Use htop to see which components use a lot of memory/cpu
Ethernet controller generates a lot of heat
Importance of different tasks

## Slide 12: Formatting the CM4 emmc
Put the CM4 into the IO Board, connect the jumper on J2: disable eMMc Boot, connect the USB slave micro USB to your PC
Download Raspberry Pi Imager and USB booter, follow this guide:
  Raspberry Pi Documentation - Compute Module hardware
  Download and run the Windows installer to install the drivers and boot tool
  Plug your host PC USB into the USB slave port, making sure you have setup the board
  Apply power to the board; Windows should now find the hardware and install the driver
  Once the driver installation is complete, run the RPiBoot.exe tool
  After a few seconds, the Compute Module eMMC will pop up under Windows as a disk
  Install the OS using the Pi imager and a custom OS from your PC (Edatec image)
Upon errors on unknown capacity of the “SD-card” as recognized by your PC, reformat using:
  On Windows go to “Create and format hard disk partitions”, select your SD card and right click the unallocated region, “New simple volume” and continue the prompts

## Slide 13: Creating new Pi images
Use a 8 GB eMMc Pi
Partition into x<<8 GB
Download Win32 Disk Imager
  Enter Boot mode for the CM4, run the USB booter (rpiboot). Once you see the pi as a disk open Win32 Disk Imager
  Select the device, set a image file location and name, enable Read only allocated partitions
  Click read
A new image for other Pi’s can be build using the Raspberry Pi Imager
  Make sure to use advanced settings to already set the name, timezone etc.

## Slide 14: Content of the image
The right Pi settings
  Enabled SSH, serial comms, Bluetooth off and all other peripherals …
Fully updated software
VS Code
Greengrass

## Slide 15: Where we want to go
Make a base image with the right configurations, image with the right host name and SSH on, AWS Greengrass already installed, the right unique IP Address
A master script looping through X Pi’s giving them the right name and default AWS Greengrass setup
Is there a way to fully configure Greengrass already in the master script?
Only OS on the eMMc and only data on the SD card
  Update raspi-config (on EEPROM) to always boot from eMMc first using the rpi-eeprom-update tool in the master script

## Slide 16: Message format
Start byte,
1 byte,
0x5A
Sensor ID,
3 bytes,
Ex.: 0x3C2A1B
Payload length,
2 bytes,
Ex.: 0x01
Payload,
N bytes,
Ex. 0x5B
Checksum,
1 byte

## Slide 17: Sensor layout
Compute module
Sensor 1
Sensor 2
Sensor 30

## Slide 18: Input signals
Block wave & Time-of-flight
Sine sweep
10 ms:
No input but still measurement
Stop
Frequency
Duration
Fixed 10V amplitude
Duration
Start
Frequency
Stop
Frequency
Fixed 10V
amplitude
Start
Frequency

## Slide 19: Reset function
CM4
Power
Splitter
P-CH mosfet
Sensor
RS485 - 1
RS485 - 2
12V, 1.5 A
12 V
3 A
12 V
1.5 A
CM4GPIO
12V
POW
12V
Sens

## Slide 20: Control using RTS RS232